## Slide 1: Construction Math Review
Megan Patent-Nygren

## Slide 2: Learning outcomes
At the end of this class you will be able to identify your ability to
  Understand order of operations
  Perform basic math operations
  Calculate fractions & ratios
  Convert units of measure
  Calculate unit weight
  Perform area and volume calculations

## Slide 3: Basic Math CALCULATIONs

## Slide 4: Order of Operations PEMDAS
2 (4 + (2+1)²) = ?
Parentheses
Exponents (4² = 4 x 4) (4³ = 4 x 4 x 4)
Multiplication
Division
Addition
Subtraction
Notes: Review the order in which mathematical operations must be calculated (PEMDAS is the acronym).
Inside to Outside
  What is in the parentheses (innermost)
  Then exponents
  Then multiply/divide
  Then add/subtract

## Slide 5: Order of operations PEMDAS
Work problems from the inside out
For example:
4 + (2+1)² = ?
4 + 3² = 4 + 9 = 13
2 (4 + (2+1)²) = ?
2 (4 + 3²)= 2 (4 + 9) = 2 (13) = 26
Notes: Work through this example with the class.

## Slide 6: Basic Math Operations Wake up you brain
See
Worksheet #1
Complete problems 1 – 7

## Slide 7: Solutions to Worksheet #1
30’ (feet)
24ft + 8ft = 32ft
43 bars
1.94mi
1.32ft
125.4 L
1700 tons
Notes: Problems 8 – 11 require more experience with translating word problems. Some students will be able to complete these, but make them optionsl. Work through any problems from the worksheet that need review.

## Slide 8: Ratio & Fractions

## Slide 9: Ratio
… is a numerical comparison between two different things.
  Can be expressed as a fraction, decimal, or %
  Examples
    3 apples to 2 oranges – 3/2 or 1.5
    5 bags cement to 10 gals water – 5/10 or .5 or 50%

## Slide 10: Ratio Example
A concrete mix has 67.5lbs of water and 150lbs of cement. What is the water to cement ratio?
67.5lbs/150lbs = .45
How much water will you need to mix with 250lbs of cement?
250lbs x .45 = 112.5lbs
Answer: you’ll need 112.5 lbs of water to mix with 250 lbs of cement.
Notes: Point out the distinction between “water to cement” and “cement to water” ratios on this & the next slide.

## Slide 11: Ratio Example (cont.)
A concrete mix has 67.5lbs of water and 150lbs of cement. What is the cement to water ratio?
150lbs / 67.5lbs = 2.222
How much cement will you need to mix with 112.5 lbs of water?
New amount of cement = 112.5 x 2.22 = 249.97
Answer: you’ll need 250 lbs of cement to mix with 112.5 lbs of water.

## Slide 12: Slope
Slopes are ratios expressed as rise/run
The first or top number is the vertical distance (rise).
The second or bottom number is the horizontal distance (run).
In this example the slope is
280/247
Notes: Provide a few common examples of slopes in their everyday work.

## Slide 13: Slope
“It has been traditional in road building organizations to refer to slope (or grade) a “run over rise”. In other words the first number indicated the length of a slope and the second number indicated the height. When the Department changed to metric in 1992, the metric version of slope was adopted. The Metric version of slope uses “rise over run”. The Departments Metric to English Conversion Committee decided in 1998 to keep this feature of the metric system while returning back to English units. This was done to keep the Departments slope reference more in keeping with today’s accepted standards.”
FL DOT Construction Math
Notes: Provide a few common examples of slopes in their everyday work.

## Slide 14: Slope
Notes: Provide a few common examples of slopes in their everyday work.

## Slide 15: Slope Examples run:rise
Run = ? Rise = 65ft slope = 3:1
Run/65ft = 3/1 R = (65ft) x 3 = 195 ft
2. Run = 42 ft Rise = 10.5 ft Slope = ? 42/10.5 = Slope = 4:1
Notes: Explain that if you are given any 2 of the measurements from the Slope = Run/Rise formula, they can calculate the 3rd measurement or number.

## Slide 16: Ratio Calculation Exercises
See
Worksheet #2
(problems 1 & 2)

## Slide 17: Solutions to Worksheet #2 (ratio problems)
1.
Step 1: 23lbs / 100gal (original amounts) = .23 (ratio)
Step 2: New salt? = 500gals x .23 = 115lbs
2.
Step 1: 30lbs (fine) to 60lbs (coarse)
Step 2: 30lbs/60lbs = .50 OR 1lb : 2lbs

## Slide 18: Fractions
… represent part or parts of a whole
  Examples ½ ¼ ¾ etc.
  Top number is called the numerator
  Bottom number is the denominator
  Adding or subtracting fractions requires a common denominator (the same number on the bottom)
  Multiplication and division does not require a common denominator (number on the bottom can be different)
  1 2 3 4
  2 4 6 8

## Slide 19: Finding the Common Denominator
1/6 + 1/3
Multiples of 6: 6, 12, 18, 24…
Multiples of 3: 3, 6, 9, 12, 15, 18…
What multiples do they share or have in common?
The LEAST or LOWEST Common Denominator
the for the fractions above is 6
Notes: These images help them see how the amount we are measuring (the slice of pizza) does not change when we slice it into more slices in order to add or subtract with “common denominators”.

## Slide 20: Finding the Common Denominator
1/6 + 2/6 = 3/6
3/18 + 6/18 = 9/18
Notes: Again, point out how we have to cut each whole (pizza) into the same number of slices before we add or subtract. However, the slice of pizza (size) does not change when we do this.

## Slide 21: Fraction examples
Addition example
  1/2 + 1/4
Step 1: create common denominator
2 · 1 1 2 1
2 · 2 4 4 4
Step 2: add numerators
2 1
4
3
4

## Slide 22: Fraction examples
Subtraction example
  1/2 - 1/4
Step 1: create common denominator
2 · 1 1 2 1
2 · 2 4 4 4
Step 2: add numerators
2 1
4
1
4

## Slide 23: Fraction examples
Multiplication example
3/16 x 1/3
Step 1: multiply numerators & denominators
3 1 3 x 1 3
16 3 16 x 3 48
Step 2: reduce fraction if possible
3
48
1
16

## Slide 24: Fraction examples
Division example
1/8 ÷ 3/16
Step 1: invert or “flip” divisor (2nd fraction) & multiply
1 3 1 16
8 16 8 3
Step 2: reduce fraction if possible
16
24
2
3

## Slide 25: Fraction Calculation Exercises
See
Worksheet #2
(problems 3 - 6)

## Slide 26: Solutions to Worksheet #2 (fractions)
3. 1/2 + 1/3 = 3/6 + 2/6 = (3 + 2) / 6
= 5/6 of a drum
4. 3/8lbs – 1/4lbs = 3/8lbs – 2/8 lbs = 1/8lbs, remove 1/8lbs aggregate
5. 1/3(sheet/diaphragm) x 6(diaphragms) = 1/3 x 6/1
= 6/3 = 2 sheets of plywood
7/8 ton ÷ 1/16 ton
7/8 ton x 16/1 ton = 14

## Slide 27: conversions

## Slide 28: Conversions
Math measurement operations have to be in same units of measurement
  (length to length)-(area to area)-(volume to volume)
Conversions differ between units
(12 inches to 1 foot)-(27 cubic feet to 1 cubic yard)-(1 inch to .08 of decimal foot)
Multiplication or division?
  If you are going to a smaller unit, multiply
    (Cubic Yards to Cubic Feet, multiply # yards by 27)
  If you are going to a bigger unit, divide
    (inches to feet, divide #inches by 12)

## Slide 29: Linear Measurement Feet to Inches
3 feet = ? Inches
48 inches = ? Feet
# feet x 12
# inches ÷ 12
36
4
Notes: These next 3 slides help them visualize and understand unites (linear, squared, cubed) as we move into geometry calculations (area, volume).

## Slide 30: Area or 2-Dimensional in² or square inches
1 foot
1 foot
1 in x 1 in

## Slide 31: Volume or 3-Dimensional in³ or cubic inches

## Slide 32: Converting Fractions to Decimals
½ same as 1 ÷ 2 same as .50
so write 1 ½ as 1.50
1/5 same as 1 ÷ 5 same as .20
write 2 1/5 as 2.20
7/16 = 7 ÷ 16 = .4375
write 5 7/16 as 5.4375
Notes: Make sure they understand these conversions before moving on.

## Slide 33: Conversion Examples
There is a bridge abutment form that is 4ft thick 4ft tall and 60ft wide. How many cubic yards will it take to fill it?
27ft3 = 1yd3 (conversion)
3 feet in each yard, 3ft x 3ft x 3ft
Step 1: 4ft x 4ft x 60ft = 960ft3
Step 2: 960ft3/27ft3 = 35.56yd3
Notes: They first need to calculate the volume by multiplying length x width x height. Because the original units are in feet, they will need to convert to cubic yards. Show them where the 27ft³ = 1yd³ conversion comes from (3ft x 3ft x 3ft). It is important that they understand linear, squared, and cubed units of measurement.

## Slide 34: Conversion Calculation Exercises
See
Worksheet #3
(problem 1 )

## Slide 35: Solutions to Worksheet #3 Conversion Problems
Step 1: 2in/12in = .167ft (converting 2 inches to feet)
Step 2: 4miles x 5280ft = 21,120ft (mile to feet)
Step 3: .167ft x 21,120ft x 24ft = 84,648.96ft3
Step 4: 84,648.96ft3/27ft3 = 3,135.15yd3

## Slide 36: Unit Weight
Weight per unit of volume
  Pound per cubic foot (pcf)
  Ton per cubic yard
  Pound per gallon

## Slide 37: Unit Weight Example
Water is 8.3lbs/gallon. You are batching concrete and you need 500lbs of water. How many gallons of water do you need?
500lbs ÷ 8.3lbs/gallon = 60.24 gallons

## Slide 38: Unit Weight Calculation Exercises
See
Worksheet #3
(problems 2 & 3)
*Provide answers in pounds and tons

## Slide 39: Solution to Worksheet #3 Unit Weight Problems
2. 4000lbs x 2.2 yd3 = 8800lbs or 4.4 tons
3. 95lbs x 240ft3 = 22,800lbs or 11.4 tons

## Slide 40: What about Word Problems?
Translating a question or request into an equation

## Slide 41: Solving Word Problems
Read problem entirely & draw diagrams
List variables, the “things” or “stuff” they are talking about
Write down the unknown, what do they want to know? What unit of measure?
Estimate answer
Identify “key” words
Write equation that mirrors problem

## Slide 42: Key words for Mathematical Operations
Addition | Increased by, more than, combine, total of, sum, added to, plus
Subtraction | Difference, decreased by, less than, fewer than, take away, how many left
Multiplication | Product of, times, of, factor of, double, triple
Division | Quotient, divided by, ratio of, per, out of, percent
Equals | Is/are, was/were, will be, gives, yields, sold for, would you have
Warning: “less than” in a word problem can be confusing. Saying “she makes $2 less than Jim (or X)” does not translate mathematically into $2 – X. Think about it. If she makes $2 less than Jim, and Jim makes $10, then
She makes $10 - $2 = $8 or X - $2

## Slide 43: Let’s solve one together
There are 12 students in the classroom. I need to break the students into 3 groups and then provide 5 word problems for each group to solve. How many students will I have in each group and how many word problems will I need to distribute?
Notes: THINK ALOUD MODELING: read the problem aloud, verbalizing thoughts and questions. “Talk” through the word problem out loud.
For example (after reading the entire problem out loud): “Ok, I have 12 students, so I’m going to circle 12 in the sentence and write 12 students down below as one of the ‘things’ or variables in the problem. Then I see that I need to break the students into 3 groups. I’ll circle 3 groups and add that to my list of variables.” etc. Until you have talked all the way through the problem, carefully modelling the step on slide 41.

## Slide 44: Word Problem Exercises
See
Word Problem
Worksheet
Notes: THINK ALOUD MODELING: read the problem aloud, verbalizing thoughts and questions. “Talk” through the word problem out loud.
For example (after reading the entire problem out loud): “Ok, I have 12 students, so I’m going to circle 12 in the sentence and write 12 students down below as one of the ‘things’ or variables in the problem. Then I see that I need to break the students into 3 groups. I’ll circle 3 groups and add that to my list of variables.” etc. Until you have talked all the way through the problem, carefully modelling the step on slide 41.

## Slide 45: Advanced calculations

## Slide 46: Advanced Calculations
  Average
  Perimeter
  Circumference
  Area
  Volume

## Slide 47: Average
Average =
The sum of all the numbers you’re averaging
The number of numbers you’re averaging
Example: What is the average foot size for a group of men who wear the following shoe sizes?
10, 11, 10, 12, 14
Average shoe size= 10 + 11 + 10 + 12 + 14 = 57 = 11.4
5 (5 shoe sizes) 5
Notes: To make sure they understand this calculation, ask them how or if this average would change if we had one more man with a size “0” foot?

## Slide 48: Average Calculation Examples
See
Worksheet #4
(complete all)

## Slide 49: Solutions to Worksheet #4
  35.29 ft
  76.38ft
  11ft

## Slide 50: Perimeter
… is the linear distance around an object
  One dimensional quantity
  Length unit of measure
  Side A+Side B+Side C+Side… until all of the sides are added together

## Slide 51: Perimeter Example: What is the perimeter of this rectangle?
4ft + 4ft + 10ft + 10ft = 28ft
Answer: the perimeter of the rectangle is 28 feet

## Slide 52: Perimeter Calculation Examples
See
Worksheet #5

## Slide 53: Solutions for Worksheet #5
3ft + 4ft + 5ft + 6ft = 18ft.
3in + 4in + 5in = 12in

## Slide 54: Circumference
… is the linear distance around a circle
π x diameter (πd)
or
2 x π x radius (2πr)
π = 3.14
(the symbol π is on your calculator)

## Slide 55: Circumference Example
A manhole has a diameter of 48 inches. What is the circumference?
Step 1. π x 48
Step 2. 3.14 x 48in = 150.72 inches
Answer: the circumference of the circle is 150.72 inches

## Slide 56: Circumference Calculation Examples
See
Worksheet #6

## Slide 57: Solutions to Worksheet #6 (circumference)
1. 2 x 3.14 x 4.5in = 28.26in
2. 3.14 x 18in = 56.52in

## Slide 58: Area

## Slide 59: Area
… is the amount of space inside the boundary of a flat (2-dimensional) object
Examples of 2-dimensional objects:
  sheet of paper
  disk
  sheet of drywall

## Slide 60: Area of Squares and Rectangles

## Slide 61: Area of a Rectangle Example
Find the area of a driveway that is 18 feet wide, 32 feet long.
A = L x W
A = 32ft x 18ft = 576ft²
Area of the driveway is 576 square feet

## Slide 62: Area of Rectangle Calculation Examples
See
Worksheet #7
(Problems 1 & 2)
Notes: You might want to give them a hint for #2 – cut that shape into 2 rectangles, then solve for each and add.

## Slide 63: Solution to Worksheet #7
1. 4yd x 7yd = 28 yd2
2. This is a 3-step problem. Separate the shape into 2 rectangles, then solve.
  Step 1: (Area of 1st rectangle) 7ft x 11ft = 77ft2
  Step 2: (Area of 2nd rectangle) 3ft x 5ft = 15ft2
  Step 3: (Add the 2 Areas together)
  77ft2 + 15ft2 = 92ft2

## Slide 64: Area of a Triangle
  … is ½ Base (b) x Height (h)
  ½ bh
  (The height is perpendicular to the base)
Notes: Spend the time to ensure that they understand how to locate the base and height of any triangle.

## Slide 65: Triangle Area Example
Find the area of a triangle to the nearest tenth of a square foot whose base (b) is 4.0 feet and whose height (h) is 10 feet.
Area = ½ bh
(½ x 4.0ft) x 10ft = 20.0ft2
Answer: The area of the triangle is 20 square feet.

## Slide 66: Area of Triangle Calculation Examples
See
Worksheet #7
(Problems 3 & 4)

## Slide 67: Solutions to Worksheet #7 (area of triangles)
A = ½ bh
3. ½ x 124.0ft x 93.5ft = 5797.0ft2
4. ½ x 75ft x 60ft = 2250ft2

## Slide 68: Area of a Circle
… is times the radius squared
Area=
= 3.14
(r² = r x r)
Notes: Clearly distinguish the difference between radius and diameter. Radius: “radiates” out from the center of the circle.

## Slide 69: Area of a Circle Example
What is the area of a retention pond that has a radius of 15 feet?
Area = x r2
3.14 x (15ft x 15ft) = 706.5ft2

## Slide 70: Area of Circle Calculation Examples
See
Worksheet #7
(problems 5 & 6)

## Slide 71: Solutions to Worksheet #7 (area of a circle problems)
3.14 x (250ft x 250ft) = 196,250ft2
or (196,350 ft²)
3.14 x (7ft x 7ft) = 153.86ft2
or (153.94 ft²)

## Slide 72: Area of a Trapezoid
…is ½ the sum of the 2 bases x height
A = ½ (b1+b2) x h

## Slide 73: Area of a Trapezoid Example
Find the area of the trapezoid below
A = ½ (b1+b2) x h
A= ½ (29ft + 13ft) x 15ft = 315ft2
A = ½ (42ft) x 15ft
A = 21ft x 15ft = 315ft2

## Slide 74: Area of Trapezoid Calculation Examples
See
Worksheet #7
(problems 7 & 8)

## Slide 75: Solutions to Worksheet #7 (area of a trapezoid)
A = ½ (b1+b2) x h
7. ½ (3ft + 6ft) x 4ft = 18ft2
8. ½ (10ft + 24ft) x 7ft = 119ft2

## Slide 76: Volume
Notes: You probably won’t have time to get to this section in a half-day class.

## Slide 77: Volume
… is the amount of 3-dimensional space an object occupies
Or, in other words
…it’s the amount of space inside a 3-dimensional object like a box, a ball, a room, etc.

## Slide 78: Volume of a Rectangular Prism
Volume = Length (L) x Width (W) x Height (H)

## Slide 79: Volume of a Rectangular Prism (box) Example
V = L x W x H
12ft x 5ft x 4ft = 240ft3

## Slide 80: Volume of a Rectangular Prism Calculation Examples
See
Worksheet #8
(problems 1 & 2)

## Slide 81: Solutions to Worksheet #8 volume of a rectangular prism
V = L x W x H
1. 14in x 19in x 11in = 2,926in3
2. 65ft x 6ft x 8ft = 3120ft3

## Slide 82: Volume of a Cylinder
Volume= πr2 x Height (h)

## Slide 83: Volume of a Cylinder Example
Volume= πr2 x h
Step 1: V = π52 x 13
Step 2: V = (3.14 x 25) x 13
Step 3: V = 1,020.5 ft³

## Slide 84: Volume of a Cylinder Calculation Examples
See
Worksheet #8
(problems 3 & 4)

## Slide 85: Solutions to Worksheet #8 (volume of a cylinder problem)
3. (3.14 x 4.9ft2) x 7.8ft = 588.05ft3
4. (3.14 x 12in2) x 34in = 15,373.44in3

## Slide 86: More Resources
NE-LTAP
https://www.khanacademy.org/math
NHI

## Slide 87: Course Evaluation
Click on the link in your email, complete the paper version, or visit: https://go.unl.edu/dd53