## Slide 1: NDOT Noise Policy and Guidance
Revisions and Updates for January 2022

## Slide 2: Why Update the Noise Policy and Guidance?
A review is required every 5 years by FHWA to ensure the accuracy and applicability of these documents are up to Federal standards.
A full content review was performed as well as cost inflation update.

## Slide 3: List of Current Revisions and Updates
Defined Noise Study Area within the Acronyms and Terms.
  Noise Guidance and Policy page iii.
Clarified numerical data rounding protocol for reporting and model validation purposes.
  Noise Guidance page 3-1 sec 3.1.2
  Guidance better reflects policy verbiage.
    Policy states, “For reporting purposes all noise level results should be rounded to the nearest whole number as part of both the impact analysis as well as the abatement analysis. For model validation purposes, modeled and field-measured noise levels will be reported to the 10th of a decibel.”
    Guidance now clearly notes that data used for model validation purposes will be rounded to the nearest 10th of a decibel, not whole number.

## Slide 4: List of Current Revisions and Updates
Revised and clarified noise study area parameters.
  Noise Guidance page 3-2 sec 3.2
  Noise Policy page 4-1 sec 4
  Revised verbiage for limits of study area and receptor placement to be clear and concise.
  Added placement for modeling receptors if none are physically located in the immediate study area.
Updated cost per unit and per benefitted receptor to account for inflation since last revision.
  Noise Guidance page 4-4 sec 4.3
  Noise Policy page 6-1 sec 6.2
  Material and construction costs were updated to reflect the current market.
    See accompanying documentation for inflation calculations.

## Slide 5: List of Current Revisions and Updates
Revised and updated “reasonableness” parameters.
  Noise Guidance page 4-5 sec 4.3.2
  Noise Policy page 6-1 sec 6.2
  Added cost tables that account for both barrier height categories
    0-16ft and 16-25ft cost tables.
  Updated example calculation with current cost data.
  Clarified categorization of costs per benefitted receptor regarding design year noise levels, barrier heights, and substantial increase in noise levels.
    Clarified circumstances in which these adjustments would be used.

## Slide 6: List of Current Revisions and Updates
Updated report submitting formats to include PDF and NDOT Sharefile.
  Noise Guidance page 6-1 sec 6.2
  “Following approval of the final noise technical report, all final TNM files and other supporting documentation specific to the noise analysis should be submitted to the NDOT Noise PQS for inclusion in the project files. All information should be provided in electronic format (e.g., pdf, NDOT Sharefile).”
Other minor clarifications and grammatical correction that did not result in significant changes in content.

## Slide 7: Traffic Noise Model 3.1
The FHWA has released Traffic Noise Model (TNM) 3.1 that includes the following features and updates:
  GIS interface
  Barrier analysis improvements
  Improved runtimes and workflows
  XML-based saving, importing, and exporting
TNM 2.5 is still acceptable for use. TNM 3.1 is available for voluntary use until FHWA updates the noise regulations at 23 CFR 772.
Before starting a noise study, please contact NDOT Noise PQS regarding which version is planned for use.

## Slide 8: Questions?
NDOT Noise Professionally Qualified Staff:
John Buhrmann
  Phone: 402-479-4766
  Email: john.buhrmann@nebraska.gov
Aaron Bedea
  Phone: 402-479-4312
  Email: aaron.bedea@nebraska.gov