SUPPLEMENTAL HYDRAULIC FINDINGS & MAINTENANCE FOR SCOUR CRITICAL BRIDGES STRUCTURE NO.: INSPECTION DATE: REPORT TYPE OPTIONS: MONITORING COUNTERMEASURES MAINTENANCE PROPOSED STRUCTURE: PROGRAM YEAR: PHOTOGRAPHS SHALL BE INCLUDED WITH THIS FORM. F MONITORING COUNTERMEASURES REASON FOR INSPECTION SUPPLEMENTAL HYDRAULIC INSPECTION: NBIS ROUTINE INTERVAL PRE STORM DURING FLOOD POST FLOOD OTHER: HYDRAULIC INSPECTOR:

INSPECTION FINDINGS

CHANGES IN CONDITIONS:

MAINTENANCE

MAINTENANCE COMPLETION DATE:

REPAIRS MADE:

REPAIRS: PERMANENT TEMPORARY

| SUBMITTED BY: | DATE SUBMITTED: |
| --- | --- |
| COPIES TO: FHWA NDOR-BRIDGE HWY. SUPT. FILE OTHER: |

NOTE:  THIS FORM IS A SUPPLEMENT TO DR385E (POA MONITORING LOG) AND IS FOR DOCUMENTING CHANGES TO THE SCOUR CONDITIONS AT THIS BRIDGE.