## Slide 1: 2016 Standards
County Roads and Municipal Streets
Neb. Rev. Stat. 39-2113
Boards - Liaison Services Section
https://dot.nebraska.gov/media/5593/nac-428-rules-regs-nbcs.pdf
Video 03
428 NAC 2
NBCS Standards
8/4/2019
Nebraska Administrative Code
Title 428
Rules and Regulations of the
Board of Public Roads Classifications and Standards
(Administrative Host: Nebraska Department of Transportation)
Notes: 8/4/2019 Updated to reflect changes per LB82 (2019). The previous version was dated12/22/2016. Slides 3 thru 7 (of the 12/22/2016 version) deleted some as a result of LB82. Slides 2, 3 (originally 8), 6 (originally 11) and 32 (originally 36) updated with minor changes. Slide 10 (originally 15) changed to 2017 Std Specs, and there were some NDOT website changes as well. Slide 15 added for Flexible Programs Requests, a direct result of LB82.
This is one of a series of videos on Nebraska’s system of
Classifying and applying standards to its highways, roads and streets.
This video provides information on the NBCS Standards, which is addressed in State Law and also in the rule and regulation Title 428 Chapter 2,
This includes - A brief overview of Minimum Design Standards, and detailed presentations on
Construction Standards
Minimum Maintenance Standards
Relaxation of Standards
And Standard Compliance Inspection Procedures
More Details on Minimum Design Standards are presented in the videos following this one.
This video also briefly addresses some other State and Federal laws and regulations, beyond Title 428, that need to be taken into account when designing and constructing highways, roads and streets.

## Slide 2: Terminology and Acronyms used in this video
NBCS = Nebraska Board of Public Roads Classifications and Standards = “The Board” = “The Board of Public Roads”
NDOT = Nebraska Department of Transportation
Standards vs. Minimum Design Standards (MDS)
Neb. Rev. Stat. = Nebraska Revised Statutes
NAC = Nebraska Administrative Code
Highways = Roads = Streets (§39-101(3), §60-624)
3R = Resurfacing, Restoration and Rehabilitation
FC = Functional Classification
CFR = Code of Federal Regulations
AASHTO = American Association of State Highway Transportation Officials
Notes: 8/4/2019 Updated to change NDOR to NDOT
First, some terminology and acronyms . . .
NBCS is the Nebraska Board of Public Roads Classifications and Standards; it may also be called the Board of Public Roads, or just The Board.
NDOT is the Nebraska Department of Transportation
Standards refers to the NBCS standards, including design, construction, maintenance and relaxation of standards. MDS refers to the Minimum Design Standards, which address only the design aspect of a work or project. Standards are often termed “minimum” but realize there are maximums (for superelevation, grade) and ranges ( for cross slopes). When we say “minimum” – sometimes it refers to all of those.
Neb. Rev. Stat. refers to the Nebraska Revised Statutes
NAC is the Nebraska Administrative Code. These are regulations, that have the force of law.
The word “Highway” in Nebraska law also refers to roads and streets. Highway means the entire width between the boundary limits of any street, road, avenue, boulevard, or way which is publicly maintained when any part is open to the use of the public for purposes of vehicular travel.
3R is short for resurfacing, restoration and rehabilitation. For more details, see the video dedicated to 3R.
FC is Functional Classification.
CFR is the acronym for the Code of Federal Regulations.

## Slide 3: Chapter 2 (428 NAC 2) Procedures for Standards
Title 428 Chapter 2
Slide 3
428 NAC 2
Notes: 8/4/2019 Updated.
Next is a brief overview of Section 001, the Minimum Design Standards, of 428 NAC Chapter 2.
For more information on the Minimum Design Standards, proceed to the next video. (the second audio media deleted)

## Slide 4: What is a Standard?
  a level of quality or attainment
  an ideal or a basis in terms of which something can be evaluated or judged
Standards
Notes: A Standard can be defined as A level of quality, or attainment,
Or an ideal or basis in terms of which something can be evaluated or judged.

## Slide 5: Minimum Design Standards are
Attributes established as acceptable by NBCS
428 NAC 2-001
Slide 5
NBCS Standards
Notes: The NBCS expresses the level, ideal, or basis, as attributes, mostly as key criteria, and sets values for each criteria depending on the general category (urban or rural), functional classification and other factors.
NOT FOR AUDIO
Standard: attributes (dimensions, speed and design loading) established as acceptable by an authority (NBCS). [A means of determining what a thing should be. Etymology: extendere (Latin), metaphoric, the royal standard coming to stand for royal authority in matters like setting weights and measures. Hence the meaning "authoritative or recognized exemplar of quality or correctness" (late 15c.). Synonyms: criterion, gauge, yardstick, touchstone. ]

## Slide 6: Design Standards - Scope County Roads and Municipal Streets
Only certain key criteria –
for safe and efficient operation
  Impractical to set standards for every possible design element or situation
428 NAC 2-001
Slide 6
Minimum Design Standards
http://www.sos.ne.gov/rules-and-regs/regsearch/Rules/Roads_Dept_of/Title-428/Chapter-2.pdf
https://dot.nebraska.gov/media/5593/nac-428-rules-regs-nbcs.pdf
or
https://dot.nebraska.gov/business-center/lpa/boards-liaison/nbcs/downloads/
which is a link on the following website:
Notes: 8/4/2019 updated (see italics below) and, in the slide itself updated the web link to 428 NAC 1 and 428 NAC 2
As it would be impractical to set standards for every design element or every situation that can be encountered,
The NBCS selected only certain, key criteria to include in the minimum design standards.
These criteria have been shown to affect safe and efficient operation of highways, roads and streets.
The Minimum Design Standards can be found online in two places:
The Secretary of State’s website under Rules and Regulations. It may be easiest to Browse Rules and Regulations by Agency. The Agency to select is RoadsTransportation, Once you are in the Transportation list, select Title 428. The MDS are in Chapter 2 of Title 428.
Another place to find NBCS standards is the Nebraska Department of Roads DOT’s website using either of the two other web links shown at the bottom of the screen. under Business Center, City/County Information, select Boards-Liaison Services Section, then select Minimum Design Standards. The link to select is “Adopted Minimum Standards (March 25, 2016).
The video following this one has more detailed information on the NBCS Minimum Design Standards.

## Slide 7
Slide 7
Why Have Design Standards?
  Safer design, driver expectations, reliability
  A primary means to achieve a high-quality product
  Determine systemwide needs
  Required by Authority
    23 CFR 625
    Neb.Rev.Stat. §39-2113
    Local Ordinances and Laws
NBCS Standards
Notes: Minimum design standards try to achieve
Safer designs,
Meet driver expectations
And Improve the reliability of the highway, road and street network
Standards are a primary means of achieving a high-quality product,
although there is a lot more to designing a road or street than just meeting minimum standards.
Standards are a way of benchmarking system-wide needs
And standards are required by authority, by
The Federal government
The Nebraska Legislature
And possibly local ordinances and laws as well.
That concludes the brief overview on Minimum Design Standards. For more detailed information, go to the next video in this series.
NOT FOR AUDIO
Jim Knott’s 2009 slide
Meeting standards:
is a primary means by which a resultant high-quality roadway will be produced. [NOT 100% FOOLPROOF AND NOT THE ONLY MEANS! – GOOD DESIGN WORK IS THE ONLY MEANS!] Designers are trained to use accepted controlling criteria throughout the project development process.
decreases the probability that safety or traffic operational problems will develop. Using design values that lie within typical ranges thus provides some quality control and a reduced risk.

## Slide 8: Conformance – The Board’s Intent
Substantial Conformance to Plans
  Limitation of construction methods
Changes over life cycle
  Natural – environmental, weather
  Man-made – wear and tear
Funding shortfalls
Failure to meet standards at every location may not be improper, or a violation, or negligence.
  Unless bad faith, or disregard of standards
428 NAC 2-001.01B, Page 2
Subsection 001.01 - Intent
Slide 8
Notes: The Board understands that construction of highways, roads and streets cannot always be completed with the accuracy that could be implied by the standards,
And that construction methods often can achieve only substantial conformance to the design.
There are various ways to measure the geometry of roads and streets, with some discretion in the selection of beginning and end points of any particular feature being measured.
Compounding this is the fact that there are changes that occur over time – including natural effects of the environment and weather, and wear and tear caused by people, including traffic.
The Board also acknowledges that there is quite often a lack of funding available to maintain or upgrade county roads and municipal streets.
It is possible that a particular roadway, after construction, does not strictly conform to the standards at each and every road or street location. Such precision was not intended by the Board. As long as it has not been done in bad faith, The Board would likely not view such occurrences as improper, as a violation of the standards, or as evidence of negligence.
It there is a clear and convincing showing that the county or municipality disregarded the standards, the Board could interpret it as a failure to meet standards.
NOT FOR AUDIO
New language inserted as a legal shield
Example: PCC paving, 12 ft lane width, 200 ft of 11 ft 10 in lane with – may be accepted.

## Slide 9: Chapter 2 (428 NAC 2) Procedures for Standards
Title 428 Table of Contents
Slide 9
428 NAC 2-002, Page 87
Notes: The next screen provides information on Nebraska’s Minimum Construction Standards
Which are covered in Section 002 of Chapter 2, on page 87

## Slide 10: Construction Standards
2017 NDOT Standard Specifications for Construction
  Required for:
    functional classifications higher than Local,
    any work or project
      on the National Highway System, or
      uses Federal funds
Non-NDOR specifications acceptable off the National Highway System
  must be “equivalent in quality” and, if so,
  submittal for NBCS approval is not required
Slide 10
Minimum Construction Standards
428 NAC 2-002, Page 87
https://dot.nebraska.gov/media/10343/2017-specbook.pdf
Notes: 8/4/2019 Updated. Changed 2007 NDOR Standard Specifications for Construction to 2017 NDOT Standard Specifications for Construction. Changes shown in italics below.
The Nebraska Department of Roads Transportation 2007 2017 Standard Specifications for Construction are
Required for highways, roads and streets with functional classifications higher than Local, or for any work or project on the National Highway System, or any project that is funded in part or entirely with Federal funds no matter what the functional classification is.
And are advisory, i.e. non-mandatory, for functional classifications Local, Scenic-Recreation Local, Minimum Maintenance and Remote Residential.
The 2007 NDOT’s Standard Specifications for Construction are online, at the web link shown on the screen.
You get to that link as follows:
From the NDOR home page, under the Business Center tab, Contractor Information
Select Contractor’s Corner. Then select Reference Manuals.
Then select the link called “2007 2017 Standard Specifications for Construction”
The regulation recognizes that a city or county may have its own standard construction specifications.
It allows those specifications to be used on city streets and county roads, in lieu of NDOR’s NDOT’s 2007 2017 Standard Specifications for Construction if those specifications are “equivalent in quality” to NDOR’s NDOT’s 2007 2017 Standard Specifications for Construction, and the work or project is not on the National Highway System.
Lack of attention to good construction standards can lead to early failure of your facility, i.e. a shortened life cycle.
That concludes this discussion on Minimum Construction Standards, 428 NAC 2-002.

## Slide 11: Chapter 2 (428 NAC 2) Procedures for Standards
Title 428 Table of Contents
Slide 11
428 NAC 2-003, Pages 88-91
Notes: The following screens provide information on Nebraska’s Minimum Maintenance Standards
Which are covered in Section 003 of Chapter 2, pages 88-91

## Slide 12: Minimum Maintenance Standards
Definition of Maintenance, p 88
Limits of Maintenance, p 88
  Nothing Extensive or Costly (428 NAC 2-003.01C5, p 89)
Physical Maintenance activities, pages 88-91
Minimum Maintenance Standards
428 NAC 2-003, Pages 88-91
Notes: Elements included in the Minimum Maintenance Standards are:
A definition of Maintenance, on page 88
Limits of Maintenance, also on page 88, the limits being necessary to emphasize that activities beyond Maintenance require the application of other standards, i.e. the Minimum Design Standards in Section 001.
The paragraph at the bottom of page 89 mentions that operations which are “extensive or costly” should not be charged to maintenance but to construction.
Routine Physical Maintenance activities are listed on pages 88-91, for roadway surfaces, shoulders and side road approaches, roadside and drainage, and structures.

## Slide 13
Address certain acts, operations or processes of repair and preservation
Keep the facility “in a condition as near as is practical” to its original constructed condition
Federal Aid projects require signed agreement – need to maintain for the life of the work/project
Recommendation:
Establish clear maintenance policies.
Minimum Maintenance Standards
Slide 13
http://www.nebraskalegislature.gov/laws/browse-chapters.php?chapter=39
http://www.nebraskalegislature.gov/laws/browse-chapters.php?chapter=60
Minimum Maintenance Standards
428 NAC 2-003, Pages 88-91
§39-101 and §60-630
Notes: Nebraska’s Minimum Maintenance Standards
Allow certain physical activities to be considered Maintenance.
  Examples: joint filling, mudjacking, cleaning out culverts, mowing, tree trimming, and many more.
The standard is to keep the highway, road or street, and all of its elements, in a condition at or near its original standard or usefulness and safety (39-101).
Take precedence over any local policy that may indicate that no maintenance is necessary, for a public road or street.
Works or Projects funded in part or entirely with Federal funds may require signing an agreement to maintain the completed facility for the life of the project.
It would be a good practice for cities and counties to establish clear maintenance policies. A policy indicating “no maintenance” would not meet the intent of State law or Title 428.
NOT FOR AUDIO
The Board’s rule 428 NAC 2.003 would be more restrictive and therefore take precedence over any policy that says “No maintenance for roads x, y and z.”

## Slide 14: Build Sidewalk Ramps
Maintenance Scope of Work
Slide 14
428 NAC 2-001.03A1c, Page 38
Notes: The 2016 standards clarified that eliminating barriers to access for the disabled as required by federal or state law, regulation or guidance - does not by itself require the application of standards higher than Minimum Maintenance.
The same goes for sidewalks and trails.
That concludes this discussion on Minimum Maintenance Standards, 428 NAC 2-003
NOT FOR AUDIO
All Presentations Slide – What Can You Do More Efficiently and Cost Effectively? – ADA work
Notes for Presenter:
ADA is a federal requirement. 3R STANDARDS IN NO WAY IMPLY THAT ADA DOES NOT HAVE TO BE MET.
From the 9/24/2015 Annual League of Nebraska Municipalities Conference
Today, ADA is an issue we all need to be aware of. We all should have, since the early 90’s, had a transition plan where all of our public buildings, all of our public spaces, sidewalks and trails – we should have had a plan to where they were all ADA compliant. We all know that you can’t do that overnight – it’s just horrifically expensive. Under the current standards, if you were just doing maintenance on city streets, a simple grind and overlay, you can’t fix and put in a ramp on the corner without invoking new and reconstructed standards. So then if you street’s too narrow, or too steep, or too sharp of curve, you couldn’t fix the sidewalk or the ramp without coming back in and doing the rest of that work. So the Board is taking it upon themselves to define, within maintenance and within 3R, you can do sidewalk repair, you can build ramps at the corner, and you do not invoke new and reconstructed standards on the rest of the street, so you can avoid some unnecessary costs plus it allows you to do your transition plan and work on some of these corners. Lincoln took the approach to say our transition plan is we can’t go in and put in a ramp on every corner, every street in Lincoln in a short period of time, but we’ll make a commitment every project we have—whether it’s a water project, wastewater or resurfacing, if we work on a street and go by a corner, we’ll fix the corner when we go by. And this is a picture (slide) of a project on North 33rd Street we did a thin resurfacing and came through and fixed the corners; however, we had to go get a relaxation because the current standards wouldn’t let us do that.
From 2015 Asphalt Conference:
Another big issue, that we obviously face, is ADA, a federal law we’re required to meet ADA, we’re required to have transition plans, we’re suppose to be fixing our sidewalks, we’re suppose to be fixing accessibility to buildings, as well as our streets and sidewalks. Today, under current minimum design standards for Maintenance or 3R, if you were just going to go in and add overlay- put a thin overlay on the street, you’ve got some broken-up sidewalk or you’ve got a corner that doesn’t have a ramp, you want to go over and fix the sidewalk and put the ramp in, you’ve just kicked yourself into doing New & Reconstructed Standards. So, by virtue of the fact that it kicks you in that and you don’t have 3R Standards, I think a lot of us struggle sometimes with doing some ADA compliance that we need to do. So, with these rules coming forward, both under 3R and under Maintenance, the Board is going to define- you can go in and do ADA fixes and ramps and repair sidewalks under Maintenance and under 3R. That’s a huge issue that allows us to go in and fix some things without necessarily being caught into a situation where we’ve got to go through and redesign the whole stretch of the roadway to reconstructed designs. Now, at the same time, I’ll also say, ADA brings regulation without funding, and to truly meet ADA on these corners in municipalities is not easy- and there is no margin for error. And while we said, you know, ADA side slope is 2%, we’ve had to actually change our design standards to 1.5(%) because if you design and build it to 2.001, we’ve had some issues where we’ve been asked to tear those out and start over on them again. We can’t afford to get there. We have been using curbs on the back of the sidewalks and small retaining walls to avoid going back into property, but these things are adding a ton of costs to our rehab projects. 3R helps a little bit on that so you’ve got some of these dollars to go ahead and do some things – other projects.

## Slide 15: Additional Design Flexibility
2019 Legislation (LB82) - §39-2113(7)
NBCS, NDOT, Counties and Municipalities cooperate to develop flexible programs
Potential for more flexibility in design and maintenance standards
  Practical design, asset preservation, context sensitive designs
Agreement documented in Memorandum of Understanding or Guidance document
Notes: 8/4/2019 Added Slide for Additional Design Flexibility
In 2019 the Legislature added a paragraph (7) to statute 39-2113
It allows the NBCS to work in cooperation with the Nebr DOT, counties and municipalities
To develop more flexibility in design and maintenance standards.
It is referring to programs and strategies such as
Practical design or flexible design that focuses funding on the primary problem or need in constructing projects that will not meet all the NBCS minimum design standards but will provide substantial overall benefit at a reasonable cost to the public,
Asset preservation or preventative maintenance that focuses on extending the life of assets, as shown by benefit cost, cost effectiveness, best value or lifecycle analyses in determining the project approach and overall benefit to the public ,
Context sensitive design that considers the established needs and values of a community that balance safety while making needed improvements in a manner that fits the surroundings and provides overall benefit to the public.
These programs must be set out in memorandums of understanding or guidance documents. In issuing such a document, the NBCS can potentially* allow project preapproval for all projects that conform to the agreed-upon program.
NOT FOR AUDIO
* “Potentially” allow project preapproval, because it will be up to the NBCS as to how widely the program will be applied. The Board may want to limit it to the county or municipality’s jurisdiction. Nebraska covers a lot of area, which varies from one end of the state to the other.

## Slide 16: Chapter 2 (428 NAC 2) Procedures for Standards How it is Organized
Title 428 Table of Contents
Slide 16
428 NAC 2-004, Pages 92-94
Notes: The next several screens provide information on Nebraska’s Relaxation of Standards requirements and process.
These are covered in Section 004 of Chapter 2, pages 92-94, including 94a and 94b
NOT FOR AUDIO
The Board is responsible for setting standards and granting or denying relaxation of standards requests.

## Slide 17: Relaxation of Standards What is it?
A documented decision that has NBCS approval to design, construct or maintain an element or segment of a highway, street or road that does not meet a requirement, value or range of values established by the NBCS standards.
Relaxation of Standards
Slide 17
Design Exception
Generally, within work termini
§39-2113
428 NAC 2-004, Pages 92-94
Notes: A relaxation of standards is a decision approved by the Board for a requirement, value or range of values in 428 NAC 2, Procedures for Standards. It applies to sections 001, 002, and 003 of Chapter 2 – Design, Construction and Maintenance standards.
“Relaxation of Standards” is the term used in state statutes.
It is the equivalent of a “Design Exception” – terminology used by the Federal government and others.
NOT FOR AUDIO
If something beyond the work termini do not meet standards, generally speaking the Board does not expect a request for a relaxation of standards.

## Slide 18: Why Would a Relaxation of Standards be Necessary?
Applying standards a special hardship due to peculiar, special or unique local situations
Many reasons, or combinations of reasons
  • Impacts to the natural environment
  • Social or right-of-way impacts
  • Preservation of historic or cultural resources
  • Sensitivity to context, or community values
  • Construction costs
Relaxation of Standards
Slide 18
§39-2113
428 NAC 2-004, Pages 92-94
Notes: To achieve a highway, road or street design that is well[-balanced (safety, operations, environmental impacts and cost), it may not always be possible to meet standards. There is a wide variety of site-specific conditions and constraints that can be encountered.
State law refers to a special hardship because of peculiar, special or unique local situations.
There can be many reasons for requesting a relaxation of standards.
It may be a severe impacts to the environment, or to something of historic or cultural value, or requiring acquisition of a lot of right-of-way. It could also be costs.
NOT FOR AUDIO
From FHWA’s Mitigation Strategies for Design Exceptions, July 2007 publication:
For many situations, there is sufficient flexibility within the design criteria to achieve a balanced design and still meet minimum values.
It must be recognized, however, that to achieve a well-balanced design (safety, operations, environmental impacts and cost), it is not always possible to meet design criteria. There is a wide variety of site-specific conditions and constraints that designers encounter. Roadways have a multitude of contexts. Establishing design criteria that cover every possible situation, each with a unique set of constraints and objectives, is not possible. On occasion, designers encounter situations in which the appropriate solution may suggest that using a design value or dimension outside the normal range of practice is necessary. Arriving at this conclusion requires the designer to understand how design criteria affect safety and operations.

## Slide 19: Who Can Request a Relaxation of Standards?
The NDOR, a county or a municipality
  §39-2113(6)
Any other interested party, for a road classified as Scenic-Recreation
  §39-2103 and §39-2113(2)
Relaxation of Standards
§39-2113
428 NAC 2-004, Pages 92-94
Slide 19
Notes: A relaxation of standards can be requested by
The NDOR
A County
A Municipality
Or, for a road classified as Scenic-Recreation, by any other interested party if the party believes that the application of Scenic-Recreation standards would defeat the purpose of the Scenic-Recreation classification (39-2103 and 39-2113(2))
NOT FOR AUDIO
39-2113
(6) Any county or municipality which believes that the application of standards for any functional classification to any segment of highway, road, or street would work a special hardship, or any other interested party which believes that the application of standards for scenic-recreation roads and highways to any segment of highway, road, or street would defeat the purpose of the scenic-recreation functional classification contained in section 39-2103, may request the board to relax the standards for such segment.

## Slide 20: What is the Process?
File the request to the Secretary of the Board.
The Secretary of the Board sets a hearing date for no later than 60 days after the filing of a complete request.
A notice is given to the requesting party at least ten (10) days prior to the hearing.
Relaxation of Standards
428 NAC 2-004D, E and F, Page 94
Timely submittal is important to avoid delays!
Notes: Filing a request with the Secretary of the Board starts the process.
The Secretary of the Board must set a hearing date for the request no later than sixty (60) days after the filing of a request that is complete. The requirements of a complete submittal will be discussed later in this presentation.
A notice confirming the date is provided to the requesting party at least ten (10) days prior to the hearing.
As you look at the possibility of up to 60 days until the hearing, note that it is important to identify the need for a relaxation of standards request as soon as you possibly can, and then promptly submit it to the Secretary of the Board. [428 NAC 2-004.01D on page 94]
That includes planning and designing a work or project. The need for a request should be determined as early in the design process as possible, hopefully in the preliminary engineering phase.

## Slide 21: What is the Process? (continued)
On the date of the hearing, the NBCS
  Considers all information submitted
  Votes (needs an affirmative vote of at least 6 Board members)
    to grant or deny, in whole or in part, or
    to continue the hearing until the next Board meeting
Decision can be appealed in accordance with the Administrative Procedures Act
Relaxation of Standards
428 NAC 2-004D, E and F, Page 94
Notes: At the hearing, the Board can grant or deny the request, in whole or in part, or continue the hearing to the next Board meeting.
The Board’s decision can be appealed.

## Slide 22: NBCS Requirements for Relaxation of Standards Requests
Thorough analysis and documentation is required
  18 basic submittal requirements
A relaxation that is granted becomes the minimum standard for that roadway segment or bridge, until circumstances change
Relaxation of Standards
428 NAC 2-004, Pages 92-94
Notes: There are a minimum of 18 requirements in order to have a complete submission for a request for a relaxation of standards. These are listed starting at the bottom of page 92, sub parts 1 through 18 ending on page 94.
There are additional requirements on page 94 for the Scenic-Recreation classification and for Low-water Stream Crossings and Fords in Parts B and C, respectively.
Whatever the Board grants for a design standard, it becomes the minimum standard for that roadway segment or bridge, until circumstances change.
This could be a change of traffic patterns and volumes, a change of functional classification and other reasons.

## Slide 23: Relaxation of MDS Required When . . .
A standard value or range or requirement in
MDS Tables
MDS Notes (requirements in bold font) – pages 47-54
cannot be met due to a special hardship.
428 NAC 2-001.03B Note 1, Page 47
Note 1 (new)
Slide 23
Notes: Regarding design standards, 428 NAC 2-001, a relaxation of standards is required if a requirement, or standard value or range cannot be met because of a special hardship.
This applies to MDS
tables
notes –
In the notes for county roads and municipal streets standards, [in 428 NAC 2-001.03B (subsection 3, part B)], on pages 47-54, the requirements and standard values are in bold font
Anything not in bold font is information and guidance for which it would not be appropriate to request a relaxation of standards

## Slide 24
Federal-aid projects may also require a Design Exception from FHWA.
Projects of Division Interest (PoDI) per FHWA/NDOR Stewardship Agreement
In Addition to a
Relaxation of Standards
Slide 24
Notes: A city or county must check with the Local Projects Section, for any Federal-aid project, to see if a Design Exception is necessary in addition to a Relaxation of Standards.

## Slide 25: Failure to Meet Standards
Penalty
10% reduction in next year’s State Allocations, for not meeting minimum standards, per §39-2121(3)
Possible loss of Federal Funds (if the work or project if funded in whole or in part with Federal funds)
Relaxation of Standards
428 NAC 2-004, Pages 92-94
Notes: The penalty for not meeting standards is a 10% reduction in next year’s Highway Allocation fund distributions.
If a work or project is funded in part, or entirely, using Federal funds, and does not meet standards, there is a risk of losing some or all of that Federal funding.
That concludes this discussion on Relaxation of Standards, 428 NAC 2-004

## Slide 26: Chapter 2 (428 NAC 2) Procedures for Standards How it is Organized
Title 428 Table of Contents
Slide 26
428 NAC 2-004, Pages 95-96
Notes: Nebraska’s Standard Compliance Inspection Procedures, Section 005 of Chapter 2, pages 95-96, allows the NBCS to check construction projects, per §39-2122,
In order to determine that minimum standards of design and construction are being met for any public highway, road or street.
This could be the result of a complaint, or a request, or just a random check.
Inspections must be scheduled at least 60 days in advance, and the county or municipality must be notified 20 days prior to the scheduled inspection.
A report is prepared within 3 working days following the inspection.
The Board must review standards compliance inspection reports within 60 days
This concludes the discussion on Standard Compliance Inspection Procedures, 428 NAC 2-005

## Slide 27: Other State and Federal Laws
Title 428 Table of Contents
Slide 27
Beyond Title 428
Notes: There are other State and Federal laws and regulations, beyond Title 428, that need to be taken into account when designing and constructing highways, roads and streets.
The following slides list some of those laws and regulations.

## Slide 28: Other Laws also apply . . .
Clean Water Act
Endangered Species Act
Americans with Disabilities Act (ADA)
Historic Preservation (Section 106)
Right-of-Way (ROW) Acquisition (Uniform Act)
etc.
Slide 28
Corps Permit
Floodplain Permit
Notes: This screen shows some other laws that may apply, from the Clean Water Act to Endangered Species Act and so on. It is not a comprehensive list!
Most of the laws shown here are Federal, although for some there may be a corollary State law, such as right-of-way acquisition laws.
Permits may be needed, such as a Corps of Engineers permit or a Floodplain permit.

## Slide 29: E&A Regulation Act
Public Works Projects – including roads and bridges involving engineering (or architecture) – must comply if project expenditures exceed $109,000 (current threshold)
Compliance means: a licensed professional engineer (or architect) provides design and construction phase services
General Information
Slide 29
http://www.ea.nebraska.gov
Neb. Rev. Stat. §§ 81-3401 – 81-3455
§ 81-3421 – Practice of Engineering
Notes: The Nebraska Engineers and Architects Act needs to be accounted for when designing and constructing public highways, roads and streets.
If a public works project involves the practice of engineering and exceeds a threshold dollar amount, it is a state law to have plans, specifications and estimates prepared, and construction observed by, an engineer licensed in Nebraska.
The practice of engineering is defined, in State statute 81-3421, as any service or creative work that requires engineering education, training, and experience in the application of special knowledge of the mathematical, physical, and engineering sciences. The services may include, but not be limited to, planning, providing studies, designs, drawings, specifications, and other technical submissions, and administering construction contracts.
The threshold dollar amount is set every fifth year by the Nebraska Board of Engineers and Architects. Refer to state statute 81-3445. The current threshold is $109,000. It is the “complete” amount of the project – design, right-of-way costs, construction, etc.
NOT FOR AUDIO
The Nebraska Board of Engineers and Architects
215 Centennial Mall South, Suite 400 P.O. Box 95165 Lincoln, Nebraska 68509-5165
Phone: 402.471.2021 Fax: 402.471.0787
Email: nbea.office@nebraska.gov
http://www.ea.nebraska.gov/when_do_you_need.html
Public Works Projects
Roads, dams, landfills, bridges, water and wastewater systems must comply with the E&A Regulation Act.
From NBEA’s website (12/29/2015):
Effective July 1, 2014, public works projects which expenditures for the complete project does not exceed $109,000 will be considered exempt from the Act. This was adjusted by the annual Consumer Price Index published by the Federal Bureau of Labor Statistics as required by § 81-3445, § 81-3449 and § 81-3453.
Licensed architects and professional engineers are required to provide design and construction phase services for all projects regulated under the Nebraska Engineers and Architects Regulation Act. These Include:
Design services including the preparation of drawings, plans, specifications, and other documents that show the features and detail of the project to be constructed.
Preparation of plans required for the permitting process. These plans must include a seal, the design professional's signature, and date. Failure to obtain the proper seal may delay the start of your project.
Construction services including visits to the project site to determine that the project is being built as designed, and that the processing of technical submissions required of the contractor is being completed.
NOT FOR AUDIO
9/16/2016 – added the words “involving engineering” after meeting with Jon Wilbeck, Executive Director of the NBEA, and LeMoyne Schulz today at NBEA offices.
9/19/2016 e-mail thread with Jon Wilbeck, Exec Dir of NBEA:
Jon, To confirm my interpretation of 81-3445 regarding the statutory threshold dollar amount ($109,000 currently, I believe), and only referring to engineering and engineers (disregarding architecture and architects in order to keep this short and simple): Only those public works projects which exceed the statutory cost threshold and which involve the practice of engineering (81-3421) are required by state law to have plans, specifications and estimates prepared, and construction observed, by a licensed engineer. Put another way: A public works project which exceeds the statutory cost threshold but does not involve the practice of engineering (81-3421) is not required by state law to have plans, specifications and estimates prepared, or construction observed, by a licensed engineer. Do you think the above statements are correct? I want to be sure the right information is presented in training for statewide highway, road and street standards. If the above interpretation is correct, even though I cannot speak for NDOR I do believe they will continue to encourage the involvement of licensed engineers in any case especially when it comes to work on structures. Thank you, and thanks again for taking the time to meet with LeMoyne and I last Friday. Regards,
Jim Wilkinson
Jim,
Both those statements appear to me to be correct.
- Jon Wilbeck
Executive Director
Nebraska Board of Engineers and Architects
402-471-3060 | jon.wilbeck@nebraska.gov
STATUTE REFERENCES
81-3421.
Practice of engineering, defined.
(1) Practice of engineering means any service or creative work that requires engineering education, training, and experience in the application of special knowledge of the mathematical, physical, and engineering sciences. The services may include, but not be limited to, planning, providing studies, designs, drawings, specifications, and other technical submissions, and administering construction contracts. The practice of engineering does not include the practice of architecture.
81-3445.
State and political subdivisions; construction projects.
Except as otherwise provided in this section and sections 81-3449 and 81-3453, the state and its political subdivisions shall not engage in the construction of any public works involving architecture or engineering unless the plans, specifications, and estimates have been prepared and the construction has been observed by an architect, a professional engineer, or a person under the direct supervision of an architect, professional engineer, or those under the direct supervision of an architect or professional engineer. This section shall not apply to any public work in which the contemplated expenditure for the complete project does not exceed one hundred thousand dollars. The board shall adjust the dollar amount in this section every fifth year. The first such adjustment after August 27, 2011, shall be effective on July 1, 2014. The adjusted amount shall be equal to the then current amount adjusted by the cumulative percentage change in the Consumer Price Index for All Urban Consumers published by the Federal Bureau of Labor Statistics for the five-year period preceding the adjustment date. The amount shall be rounded to the next highest one-thousand-dollar amount.
Source
Laws 1997, LB 622, § 45;
Laws 1999, LB 253, § 2;
Laws 2004, LB 599, § 2;
Laws 2011, LB45, § 11.
81-3453.
Practice of engineering; exempted activities.
The provisions of the Engineers and Architects Regulation Act regulating the practice of engineering do not apply to the following activities:
(1) The construction, remodeling, alteration, or renovation of a detached single-family through four-family dwelling of less than five thousand square feet above grade finished space. Any detached or attached sheds, storage buildings, and garages incidental to the dwelling are not included in the tabulation of finished space. Such exemption may be increased by rule and regulation of the board adopted pursuant to the Negotiated Rulemaking Act but shall not exceed the Type V, column B, limitations set forth by the allowable height and building areas table in the state building code adopted in section 71-6403;
(2) The construction, remodeling, alteration, or renovation of a one-story commercial or industrial building or structure of less than five thousand square feet above grade finished space which does not exceed thirty feet in height unless such building or structure, or the remodeling or repairing thereof, provides for the employment, housing, or assembly of twenty or more persons. Any detached or attached sheds, storage buildings, and garages incidental to the building or structure are not included in the tabulation of finished space. Such exemption may be increased by rule and regulation of the board adopted pursuant to the Negotiated Rulemaking Act but shall not exceed the Type V, column B, limitations set forth by the allowable height and building areas table in the state building code adopted in section 71-6403;
(3) The construction, remodeling, alteration, or renovation of farm buildings, including barns, silos, sheds, or housing for farm equipment and machinery, livestock, poultry, or storage and if the structures are designed to be occupied by no more than twenty persons. Such exemption may be increased by rule and regulation of the board adopted pursuant to the Negotiated Rulemaking Act but shall not exceed the Type V, column B, limitations set forth by the allowable height and building areas table in the state building code adopted in section 71-6403;
(4) Any public works project with contemplated expenditures for the completed project that do not exceed one hundred thousand dollars. The board shall adjust the dollar amount in this subdivision every fifth year. The first such adjustment after August 27, 2011, shall be effective on July 1, 2014. The adjusted amount shall be equal to the then current amount adjusted by the cumulative percentage change in the Consumer Price Index for All Urban Consumers published by the Federal Bureau of Labor Statistics for the five-year period preceding the adjustment date. The amount shall be rounded to the next highest one-thousand-dollar amount;
(5) Any alteration, renovation, or remodeling of a building if the alteration, renovation, or remodeling does not affect architectural or engineering safety features of the building;
(6) The teaching, including research and service, of engineering subjects in a college or university offering an ABET-accredited engineering curriculum of four years or more;
(7) A public service provider or an organization who employs a licensee performing professional services for itself;
(8) The practice by a qualified member of another legally recognized profession who is otherwise licensed or certified by this state or any political subdivision to perform services consistent with the laws of this state, the training, and the code of ethics of such profession, if such qualified member does not represent himself or herself to be practicing engineering and does not represent himself or herself to be a professional engineer;
(9) The offer to practice engineering by a person not a resident of and having no established place of business in this state if the person is legally qualified by licensure to practice engineering in his or her own state or country. The person shall make application to the board in writing and after payment of a fee established by the board may be granted a temporary permit for a definite period of time not to exceed one year to do a specific job. No right to practice engineering accrues to such applicant with respect to any other work not set forth in the permit;
(10) The work of an employee or a subordinate of a person holding a certificate of licensure under the Engineers and Architects Regulation Act or an employee of a person practicing lawfully under subdivision (9) of this section if the work is done under the direct supervision of a person holding a certificate of licensure or a person practicing lawfully under such subdivision;
(11) Those services ordinarily performed by subordinates under direct supervision of a professional engineer or those commonly designated as locomotive, stationary, marine operating engineers, power plant operating engineers, or manufacturers who supervise the operation of or operate machinery or equipment or who supervise construction within their own plant;
(12) Financial institutions making disbursements of funds in connection with construction projects;
(13) Earthmoving and related work associated with soil and water conservation practices performed on farmland or any land owned by a political subdivision that is not subject to a permit from the Department of Natural Resources or for work related to livestock waste facilities that are not subject to a permit by the Department of Environmental Quality;
(14) The work of employees and agents of a political subdivision or a nonprofit entity organized for the purpose of furnishing electrical service performing, in accordance with other requirements of law, their customary duties in the administration and enforcement of codes, permit programs, and land-use regulations and their customary duties in utility and public works construction, operation, and maintenance;
(15) Work performed exclusively in the exploration for and development of energy resources and base, precious, and nonprecious minerals, including sand, gravel, and aggregate, which does not have a substantial impact upon public health, safety, and welfare, as determined by the board, or require the submission of reports or documents to public agencies;
(16) The construction of water wells as defined in section 46-1212, the installation of pumps and pumping equipment into water wells, and the decommissioning of water wells, unless such construction, installation, or decommissioning is required by the owner thereof to be designed or supervised by an engineer or unless legal requirements are imposed upon the owner of a water well as a part of a public water supply;
(17) Work performed in the exploration, development, and production of oil and gas or before the Nebraska Oil and Gas Conservation Commission; and
(18) Siting, layout, construction, and reconstruction of a private onsite wastewater treatment system with a maximum flow from the facility of one thousand gallons of domestic wastewater per day if such system meets all of the conditions required pursuant to the Private Onsite Wastewater Treatment System Contractors Certification and System Registration Act unless the siting, layout, construction, or reconstruction by an engineer is required by the Department of Environmental Quality, mandated by law or rules and regulations imposed upon the owner of the system, or required by the owner.
Source
Laws 1997, LB 622, § 53;
Laws 1999, LB 253, § 4;
Laws 1999, LB 440, § 2;
Laws 2000, LB 900, § 252;
Laws 2003, LB 94, § 19;
Laws 2004, LB 599, § 5;
Laws 2011, LB45, § 17;
Laws 2015, LB23, § 48.

## Slide 30: Review and Questions
428 NAC 2
Procedures for Standards
Classification and Standards
Slide 30
Notes: This final segment is a short review of what was discussed in this video, with questions.
When it comes time to answering a review question, you have the option of pausing the video before the answer is given.

## Slide 31: Review
Review of Board’s (NBCS) responsibilities:
  Sets specific criteria for Functional Classification categories
  Hears appeals of Functional Classification assignments
  Sets Minimum Standards (Design, Construction, Maintenance)
  Acts on Relaxation of Standards requests
  All of the above
State Law
Neb. Rev. Stat. §39-2109(1)
Neb. Rev. Stat. §39-2111
Neb. Rev. Stat. §39-2113
Neb. Rev. Stat. §39-2113(5) and (6)
Slide 31
Notes: State law assigns which responsibility or responsibilities to the NBCS?
Answer: E

## Slide 32: Review Questions
Minimum Maintenance Standards do not apply beyond the curb or shoulder? T or F
Application of NDOT’s 2017 Standard Specifications for Construction, or specifications equivalent in quality*, are required for a road or street classified as a Collector . T or F
The Board of Engineers and Architects dollar threshold applies only to the estimated construction amount. T or F
428 NAC 2-003, Pages 88-92
428 NAC 2-002, Page 87
§81-3401 - §81-3455
Slide 32
* Roads and Streets not on the National Highway System
Notes: False. Maintenance applies to all elements of a highway, road or street. Including surface, shoulders, roadsides, traffic control devices, structures, waterways, and drainage facilities
True. It is true for any functional classification above Local – which means Collector, Other Arterial, Major Arterial, Expressway and Interstate. It may also apply to Federal-aid projects.
False. The threshold amount, $109.000 as of December, 2016, applies to the entire project cost including but not limited to design, right-of-way acquisition costs, utility relocation costs, construction and construction inspection.

## Slide 33: 2016 Standards
County Roads and Municipal Streets
Neb. Rev. Stat. 39-2113
Boards - Liaison Services Section
  https://dot.nebraska.gov/media/5593/nac-428-rules-regs-nbcs.pdf
Video 03
428 NAC 2
NBCS Standards
8/4/2019
Notes: This video provided information on the NBCS Standards, which is addressed in State Law and also in the rule and regulation Title 428 Chapter 2,
This includes – A brief overview of Minimum Design Standards, and detailed presentations on
Construction Standards
Minimum Maintenance Standards
Relaxation of Standards
And Standard Compliance Inspection Procedures
More Details on Minimum Design Standards are presented in the videos following this one.
This video also briefly addressed some other State and Federal laws and regulations, beyond Title 428, that need to be taken into account when designing and constructing highways, roads and streets.